## Slide 1: Bray Team Week 3 Update
Avery Haynes, Locke Lehmann, Travis Carlson, Cody Sims, Zachary Walker, Michael Hager
2/5/2024

## Slide 2: Weekly Deliverables
Tasks | Lead | Percentage Done | Notes
Formulate experimental design for testing | Locke/Avery | 100% | Completed
Peer Evaluation | All | 100% | Completed
Set up sensors in valves/ actuator | Cody/Travis | 30% | First round of supplies arrived, second round to be purchased. Start date TBD by team soon.
Research data analysis methods | Michael | 60% | Have valid research for methods to analyze data with Raspberry Pi.

## Slide 3: Experimental design: Potentiometer
Hypothesis: Design can achieve below 2% error from the actual rotational position of the ball valve under various temperature conditions.
Independent Variables: Rotational position of the valve, surrounding temperature
Dependent variables: % Error

## Slide 4: Experimental design: Hall effect sensor
Hypothesis: Design can achieve below 2% error from the actual rotational position of the ball valve/butterfly valve under various temperature conditions.
Independent Variables: Rotational position of the valve, surrounding temperature, distance between hall effect sensor and magnet.
Dependent variables: % Error
Initial distance testing: 0, 2, 4, 6, 8 ,10 mm

## Slide 5: Experimental Design: Bolt Strain Gauge
Hypothesis: Design can achieve below 5% error from the actual torque of the actuator under various temperature and pressure conditions.
Independent variables: Temperature, Pressure
Dependent variables: % error

## Slide 6: Experimental Design: Motor EMF
Hypothesis: Design can achieve below 5% error from the actual torque of the actuator under various temperature and pressure conditions.
Independent variables: Temperature, Pressure
Dependent variables: % error

## Slide 7: Experimental Design: Combined Concepts
Hypothesis: Design concepts together still achieve the required error percent while under various pressures
Independent variables: pressure
Dependent variables: torque, position, error%
Will Temperature test at room temp, 100℉, and 40℉

## Slide 8: Budget/Materials Update
First parts ordered 1/15/24 (arrived, thru much confusion)
  For testing position deliverable & collecting data ($128.27)
Asked Bray during today’s call to send materials for:
  Activating & toggling actuators
  Vice to support valves during testing
  Exact hall effect sensor used in their traditional products
Will order supplies for torque deliverables this week
  Bolt strain gauges, motor head & belt, additional casing, hall effect sensor

## Slide 9: Gantt Chart

## Slide 10: Next Week's Deliverables
Tasks | Lead | Percentage Done | Notes
Test sensor setup with valves and actuators | Cody/Travis | 0% | Upon arrival of all supplies, begin system setup and follow test plan.
Build frame for valve and actuator | Zack/Michael | 5% | Start building frame for when parts arrive for testing.
Purchase remaining parts | Avery | 25% | Have talked with Bray, will do a final run through to see if we need to order anything else