## Slide 1: Bray Team Project Update
Avery Haynes, Locke Lehmann, Travis Carlson, Cody Sims, Zachary Walker, Michael Hager
9/22/2023

## Slide 2: Current/Upcoming Tasks
Research Topics/Deliverables:
Brainstorming ideas for detecting true valve position/torque
Function Chain
Review SolidWorks parts and assemblies (are there more to send?)
Narrow down concepts

## Slide 3: House of Quality
Is this helpful?
Maybe for narrowing down concepts and seeing if they fit the criteria

## Slide 4: Black Box Model
Sense true valve Position
Mechanical and Electrical Energy
Electrical Energy
Data

## Slide 5: Brainstorming
Actuator output torque deliverable

## Slide 6: Brainstorming
True valve position deliverable

## Slide 7: Strain Gauges
Full Bridge Gauge configuration to sense torque:
Measures shaft torsion
Could be attached to any stationary part against the stop bars that receives a torque
Cylindrical Strain Gauges:
Placed inside a fixed fastener
Measures axial loads, not torsional
Could be placed on a stop bar. (inside the rotating shaft?)
Washer Strain Gauges:
Used in place of a washer in a fastener assembly
Measures axial loads
Placed inline with stop bars
Rotational Torque Sensor:
Direct torque measurement
Rotary transducer & slip ring mounted in-line with shaft
Mounted between actuator and valve stem